Nota, se metto a terra RX no nva ..

I an using a 5V Arduino Nano which of course is 5V. The Esp8266 is a 3.3v device and so I am using a voltage divider to bring the Arduinos 5V down to 3.3v. If you are using a 3.3v Arduino then you do not need the voltage divider.
The wiring is very similar to the FTDI.
Arduino pin 3 to voltage divider and then to ESP8266 RX
Arduino pin 2 to ESP8266 TX
Arduino GND to ESP8266 GND
Pull CH_PD HIGH with a 10K resistor to +3.3v
+3.3V to vcc
You only need the voltage divider on the Arduino TX pin. The 5V Arduino will read 3.3v as HIGH so you can connect the ESP8266 TX pin directly to the Arduino RX pin.
Make sure the ESP8266 has enough current. If it does not it may keep resetting and may not broadcast a signal.
Arduinos cannot supply enough current and you should use a separate power supply. While experimenting I use a bread board power supply.
I am using a simple serial in, serial out sketch.
// Basic serial communication with ESP8266 / // Uses serial monitor for communication with ESP8266 / // / // Pins / // Arduino pin 2 (RX) to ESP8266 TX / // Arduino pin 3 to voltage divider then to ESP8266 RX / // Connect GND from the Arduiono to GND on the ESP8266 / // Pull ESP8266 CH_PD HIGH / // / // When a command is entered in to the serial monitor on the computer / // the Arduino will relay it to the ESP8266 / // / #include <SoftwareSerial.h> / SoftwareSerial ESPserial(2, 3); // RX | TX / void setup() / { / Serial.begin(9600); // communication with the host computer / //while (!Serial) { ; } / // Start the software serial for communication with the ESP8266 / ESPserial.begin(9600); / Serial.println(""); / Serial.println("Remember to to set Both NL & CR in the serial monitor."); / Serial.println("Ready"); / Serial.println(""); / } / void loop() / { / // listen for communication from the ESP8266 and then write it to the serial monitor / if ( ESPserial.available() ) { Serial.write( ESPserial.read() ); } / // listen for user input and send it to the ESP8266 / if ( Serial.available() ) { ESPserial.write( Serial.read() ); } / }

Once everything is setup, open the serial monitor and cycle the power on the ESP8266 and you should receive the welcome message.