# LINKS
http://williamdurand.fr/2015/03/17/playing-with-a-esp8266-wifi-module/
questo sembra ok
https://blogs.msdn.microsoft.com/abhinaba/2016/01/23/esp8266-wifi-with-arduino-uno-and-nano/
# WiFi Serial Transceiver Module w/ ESP8266
# ESP-01
## Overview
ESP8266 is a highly integrated chip designed for the needs of a new connected world. It offers a complete and self-contained Wi-Fi networking solution, allowing it to either host the application or to offload all Wi-Fi networking functions from another application processor.
ESP8266 has powerful on-board processing and storage capabilities that allow it to be integrated with the sensors and other application specific devices through its GPIOs with minimal development up-front and minimal loading during runtime. Its high degree of on-chip integration allows for minimal external circuitry, and the entire solution, including front-end module, is designed to occupy minimal PCB area.
In this tutorial, we’ll use a seeeduino to control the ESP8266 WiFi module to request a static page from the internet. This is a basic use of TCP socket, for other usage, please refer to the AT command guide of the module.
## Material list
- Seeeduino V3 / Arduino Uno
- ESP8266 Serial WiFi module
- UartSBee v4 / other USB to TTL converter
Note： We used a software serial to print some debugging information as there’s only one hardware serial on seeeduino board. But the limitation of software serial is that it can’t communicate in a higher baud rate than 19200. So part of the output from ESP module will be dropped because the baud rate 57600 of ESP module is higher than that of the software serial. If you have a board with more than one hardware serial (e.g. Arduino Mega 2560), the case will be easier.
## Step 1 – Connection

## Step 2 – Programming
1. Open Arduino IDE and create a new sketch;
2. Parse the following code into the sketch editor (need modifying the SSID and PASS macros into your own situation);
1	#include <SoftwareSerial.h>

2	#define SSID "xxxxxxxx"

3	#define PASS "xxxxxxxx"

4	#define DST_IP "220.181.111.85" //baidu.com

5	SoftwareSerial dbgSerial(10, 11); // RX, TX

6	void setup()

7	{

8	// Open serial communications and wait for port to open:

9	Serial.begin(57600);

10	Serial.setTimeout(5000);

11	dbgSerial.begin(9600); //can't be faster than 19200 for softserial

12	dbgSerial.println("ESP8266 Demo");

13	//test if the module is ready

14	Serial.println("AT+RST");

15	delay(1000);

16	if(Serial.find("ready"))

17	{

18	dbgSerial.println("Module is ready");

19	}

20	else

21	{

22	dbgSerial.println("Module have no response.");

23	while(1);

24	}

25	delay(1000);

26	//connect to the wifi

27	boolean connected=false;

28	for(int i=0;i<5;i++)

29	{

30	if(connectWiFi())

31	{

32	connected = true;

33	break;

34	}

35	}

36	if (!connected){while(1);}

37	delay(5000);

38	//print the ip addr

39	/*Serial.println("AT+CIFSR");

40	dbgSerial.println("ip address:");

41	while (Serial.available())

42	dbgSerial.write(Serial.read());*/

43	//set the single connection mode

44	Serial.println("AT+CIPMUX=0");

45	}

46	void loop()

47	{

48	String cmd = "AT+CIPSTART=\"TCP\",\"";

49	cmd += DST_IP;

50	cmd += "\",80";

51	Serial.println(cmd);

52	dbgSerial.println(cmd);

53	if(Serial.find("Error")) return;

54	cmd = "GET / HTTP/1.0\r\n\r\n";

55	Serial.print("AT+CIPSEND=");

56	Serial.println(cmd.length());

57	if(Serial.find(">"))

58	{

59	dbgSerial.print(">");

60	}else

61	{

62	Serial.println("AT+CIPCLOSE");

63	dbgSerial.println("connect timeout");

64	delay(1000);

65	return;

66	}

67	Serial.print(cmd);

68	delay(2000);

69	//Serial.find("+IPD");

70	while (Serial.available())

71	{

72	char c = Serial.read();

73	dbgSerial.write(c);

74	if(c=='\r') dbgSerial.print('\n');

75	}

76	dbgSerial.println("====");

77	delay(1000);

78	}

79	boolean connectWiFi()

80	{

81	Serial.println("AT+CWMODE=1");

82	String cmd="AT+CWJAP=\"";

83	cmd+=SSID;

84	cmd+="\",\"";

85	cmd+=PASS;

86	cmd+="\"";

87	dbgSerial.println(cmd);

88	Serial.println(cmd);

89	delay(2000);

90	if(Serial.find("OK"))

91	{

92	dbgSerial.println("OK, Connected to WiFi.");

93	return true;

94	}else

95	{

96	dbgSerial.println("Can not connect to the WiFi.");

97	return false;

98	}

99	}

--------------------------------------------------------------------------------
## Connecting the ESP8266 to an Arduino
The steps you need to take are simple. This is written for the ESP8266-01 but you can find the pinout for other models easily and use the same pins. First we will connect the Arduino UNO to a breadboard:
1. Connect the Arduino’s 3v3 (3.3V) output to the red line on a breadboard. The ESP8266 works with 3.3V and not 5V, so this is necessary. If you want to connect other components that use 5V, you can connect the 5V output to the other red line of the breadboard, just make sure you don’t connect the two.
2. Connect GND (ground) to the blue line.
3. Connect the RES or RESET pin to the blue line. When you ground the reset pin, the Arduino works as a dumb USB to serial connector, which is what we want to talk to the ESP8266.
4. Connect the RXD pin of the Arduino to the RX pin of the ESP8266 (yellow color in the picture).
5. Connect the TXD pin of the Arduino to the TX pin of the ESP (green color in the picture). Usually, when we want two things to talk to each other over serial, we connect the TX pin of one to the RX of the other (send goes to receive and the opposite). Here we do not have the Arduino talk to the ESP8266 though, our computer is talking to it via the Arduino.
6. Connect the GND pin of the ESP to the blue line and the VCC pin to the red line.
7. Finally CH_PD goes to the red line, supposedly it will not work if you do not connect this. According to a discussion I found:
ESP-01 and ESP-03 were initially meant to be used as an Arduino WiFi module. In that aspect it made sense to break out CH_PD so that the user could disable the device when not in use (to save power).

## Using the Arduino IDE
In the Arduino IDE, you don’t need to choose a board, as we’re not uploading anything to the ESP8266. Just choose the right port in the Tools menu and go to Tools → Serial Monitor. Then simply set your baud rate to 115200 (the default ESP8266 firmware uses it) and your line endings to Both NL & CR.
If you type AT in the message field and press enter, it should respond with OK.
And since we ta